## Slide 1
SIGNIFICANCE OF DRAINAGE MEASURES IN LANDSLIDE MITIGATION-CASE STUDIES
Dr. Ratnakar R. Mahajan
Deputy General Manager
Maccaferri Environmental Solutions Pvt. Ltd.

## Slide 2: MAJOR CASUES OF LANDLSIDE
    Steep gradients
    Sudden increase in overburden or other loads
    Continuous rainfall (leading to flash floods, toe erosion near river slopes, etc.) and Glacier melting
    Deforestation
    Increased pore water pressure
    Seismic activity
Improper Drainage
Mitigation cannot begin without investigating the various factors that triggers the landslide

## Slide 3
2. Increase the resisting forces
Buttressing
Retaining structures
Reinforced soil slope and walls
Surface slope protection
Slope improvement
Reinforcement
Soil nailing
Micropiles
Anchors
1. Avoid or eliminate the problem itself
Facility relocation
Complete removal of slides
Bridging
Tunneling
SYSTEMS FOR LANDLSIDE MITIGATION
Surface drainage
Sub surface drainage
Excavation
Light weight fill materials
Drainage systems
Unloading
3. Reduce the driving forces
Drainage measures alone may not sufficient to improve slope stability, so drainage measures are adopted in conjunction with other methods based on the site specific requirement.
Notes: Drainage helps in landslide mitigation by reducing pore pressures within the soil, thereby increasing effective stress and shear strength; and (2) by reducing the driving forces of water pressures in cracks

## Slide 4
DIFFERENT DRAINAGE MEASURES
Surface drainage measures
Catch water or interceptor drains-drains provided on hill slopes to intercept water flowing from upper reaches (more or less parallel to the road)
Chute/cascade - The water entrapped in the catch water drains is so brought down
Road Side drains

## Slide 5
DIFFERENT DRAINAGE MEASURES
Subsurface Drainage measures
Aims at improving slope stability by controlling pore water pressures within the slope
Horizontal drains
Cut-off drains
Drainage trenches
Drain blankets
Relief wells
Internal drains of retaining soil structures
Chimney drain/Drainage geocomposite

## Slide 6
landslide case studies highlighting drainage

## Slide 7
The Ministry of Road Transport & Highways
Rehabilitation/Treatment of landslide locations with slope protection and drainage improvement
Package-I include following locations:-
1.Nandprayag (200m)
2.Maithana (350m)
3.Birahi (100m)
4.Gulabkothi (125m)
Package-II include following locations:-
1.Helang (275m)
2.Govindghat-II (150m)
3.Govindghat-III (150m)

## Slide 8: STAKEHOLDERS INVOLVED
CLIENT
PROOF CHECKING CONSULTANT
RG Buildwell Engineers Ltd
TECHNOLOGY PARTNER
SAFETY CONSULTANT
M/s Khanna Goyal Designers
AUTHORITY ENGINEER
PIU, Dehradun
DPR CONSULTANT

## Slide 9: PROBLEM DESCRIPTION & CAUSATIVE FORCES
Debris material from old slide
Surface Erosion
LOCATION: BIRAHI

## Slide 10
SOLUTION PROVIDED – LOCATION: BIRAHI
Chute drain
Road side drain
Existing culvert
Toe drain
Reinforced soil structure
Gabion wall
Bioengineering measures (Macmat R)
Surface anchors
Notes: Birahi 2m * 2m

## Slide 11
SOLUTION PROVIDED – LOCATION: BIRAHI
Road side drain
Toe drain
Drainage composite

## Slide 12
SOLUTION PROVIDED; DRAINAGE SCHEME – LOCATION:BIRAHI
Chute drain
Road side drain
Existing culvert
Toe drain

## Slide 13: PROBLEM DESCRIPTION & CAUSATIVE FORCES
Heavy jointed rock mass with prominent weakness planes
Increase of pore water pressure in joints
LOCATION: GULABKOTI

## Slide 14
SOLUTION PROVIDED – LOCATION: GULABKOTI
Secured drapery

## Slide 15
Toe erosion due to river
Steep slope
Valley side
LOCATION: GOVINDGHAT II
PROBLEM DESCRIPTION & CAUSATIVE FORCES
Hill side

## Slide 16
SOLUTION PROVIDED – LOCATION: GOVINDGHAT II
Existing culvert
Catch water drain
Road side drain
Bioengineering measures (profile)
Gabion wall
Reinforced soil structure
Gabion mattress

## Slide 17
SOLUTION PROVIDED; DRAINAGE SCHEME – LOCATION: GOVINDGHAT II
Existing culvert
Catch water drain
Road side drain

## Slide 18: PROBLEM DESCRIPTION & CAUSATIVE FORCES
Subsurface run off water causes removal of fines
Improper drainage
Formation of nalla
Hill side
LOCATION: MAITHANA

## Slide 19
SOLUTION PROVIDED– LOCATION: MAITHANA
Gabion toe wall –scour protection
Gabion mattress
Gabion wall
Reinforced soil wall
Hydroseeding
Self drilling anchors + Drapery

## Slide 20
SOLUTION PROVIDED– LOCATION: MAITHANA
Hydroseeding+ SDA
Reinforced soil structure
Gabion wall

## Slide 21
SOLUTION PROVIDED; DRAINAGE SCHEME – LOCATION: MAITHANA
RCC box culvert
Stepped chute Drain
Gabion Cascade
Road side Drain
Stepped chute drain

## Slide 22
SOLUTION PROVIDED; DRAINAGE SCHEME – LOCATION: MAITHANA
Gabion Cascade
Stepped chute drain

## Slide 23: PROBLEM DESCRIPTION & CAUSATIVE FORCES
Rock mass failure
LOCATION: HELANG

## Slide 24
Reinforced soil structure
Bioengineering solutions
Simple drapery
Rockfall Barrier
Gabion cascade
Drainage geocomposite
SOLUTION PROVIDED – LOCATION: HELANG

## Slide 25
SOLUTION PROVIDED; DRAINAGE SCHEME – LOCATION: HELANG
Gabion cascade
Road side drain
Existing culvert
Chute drain

## Slide 26
RCC Box Culvert
Stepped chute drain
Road side drain
SOLUTION PROVIDED; DRAINAGE SCHEME – LOCATION: HELANG

## Slide 27: ` DRAINAGE DESIGN
Type of Specific Drainage Works Required:
Chute drain
Catch water drains
Road side drain
Box culvert

## Slide 28: Parameters required for drainage design
Determination of Rainfall data (IRC-SP-042)
Determination of Catchment Area (IRC-SP-042)
Determination of peak runoff (Hydrological Study)
Hydraulic Design (IRC-SP-042 )
Location of Culverts, Catch drain & Chute drain

## Slide 29: Drainage Design
1. Calculation of Rainfall intensity ( IRC SP13, Page 22)
As per Indian Meteorological Department (IMD), Rainfall in the State of Uttarakhand between 15 June and 18 June 2013 was measured at 385.1 mm against normal rainfall of 71.3 mm, which was in excess by 440%. India Disaster Report, Page 22. NIDM- 2013
Frequency of Rainfall= 385.1mm for 3 days
i.e = 128.4 mm for 24 hrs
Uttarakhand Landslide Projects - Glimpses of Drainage Measures

## Slide 30: Drainage Design
2. Determination of Catchment Area (Delineation from Satellite imagery and GIS )
Uttarakhand Landslide Projects - Glimpses of Drainage Measures

## Slide 31: Drainage Design
3. Determination of Peak Runoff (Hydrological Study- IRC SP42, Page 64)
As per Indian Meteorological Department (IMD), Rainfall in the State of Uttarakhand between 15 June and 18 June 2013 was measured at 385.1 mm against normal rainfall of 71.3 mm, which was in excess by 440%. India Disaster Report, Page 22. NIDM- 2013
Q=0.028 * P* i* A
Q= Discharge in Cumecs (m3/s)
P= Runoff Co-efficient= 0.8
i= rainfall intensity= 6.8 cm/hr
A= 48.30 hectares
Q = 7.2 m3/s
Uttarakhand Landslide Projects - Glimpses of Drainage Measures

## Slide 32: Drainage Design
4. Hydraulic Design (IRC-SP-042 )
We know
Discharge through hill slope
Total height of valley side
We need to know
Width of section
Height of section
Depth of stilling basin
Requirement of Stilling Basin
Slope of channel
Slope of bed
Uttarakhand Landslide Projects - Glimpses of Drainage Measures

## Slide 33: Drainage Design
4. Hydraulic Design (IRC-SP-042 )
Assume,
Base width of Trapezoidal section to be 1.2 m
Manning’s Roughness Co-efficient of 0.013
By Trial and Error Method,
Depth of flow y1= 0.232m
Velocity
= 15.4 m/s
Bed slope of S=1 (<450)
Channel slope of 1:z = 1:0.36
Uttarakhand Landslide Projects - Glimpses of Drainage Measures

## Slide 34
4. Hydraulic Design (IRC-SP-042 )
To know the type of flow we need to calculate Froude’s number (Fr)
Fr is a dimensionless value that describes different flow regimes of open channel flow
V = Velocity of Flow
D = Hydraulic depth
g = Gravity= 9.81 m/s2.
Fr = 1 Critical flow,
Fr > 1 Supercritical flow (fast rapid flow)
Fr < 1 Subcritical flow (slow / tranquil flow)
Fr = 8.4
After determining type of flow, Find height of Hydraulic Jump (Y2) (USBR, Page 7 & IS:4997:1968, Page 6)
Y2 = 2.6 m
After height of Hydraulic Jump, we need to calculate Length of Hydraulic Jump
LB = 2.5 m

## Slide 35
Due to large height of flow of water, stilling basin is required at every 15 m to dissipate energy
Side of Chute drain is kept as 0.6 m based on depth of flow of water
Side walls of Stilling Basin is kept as 2m to accommodate the hydraulic jump
Depth of stilling basin 2.75 m to accommodate the hydraulic jump
Length of Stilling Basin is kept at 2.5m to account for the safe flow of water after the Hydraulic Jump Depth
Uttarakhand Landslide Projects - Glimpses of Drainage Measures

## Slide 36
What if chute drain do not performs?
Water flow destroys everything on its way
Scouring, Erosion, Landslide, etc
Uttarakhand Landslide Projects - Glimpses of Drainage Measures
Construction Feasibility
Site conditions has to be considered before finalizing the design parameters
Base width of Channel, slope of channel, alignment of channel etc has to be considered
Timing of construction-pre monsoon/post monsoon to be dates to be checked

## Slide 37: CONSTRUCTION PHOTOGRAPHS- LOCATION: HELANG
Chimney Drain

## Slide 38: CONCLUSION
Drainage-an inevitable part of landslide mitigation
Main drainage measures which are suitable for Uttarkhand Landslide mitigation are Catchwater drains , Chute drains , longitudinal road drains , chimney drains and culverts.
Drains are to be designed as per types of drains and type of flow .
Construction feasibility should be a major consideration , while finalising the dimensions of drain .

## Slide 39: THANKS FOR YOUR KIND ATTENTION